## Slide 1
Chapter Presenter
Traffic Pattern
The development of this program was made possible in part by a generous donation from the Sporty’s Foundation.

## Slide 2
Session Objectives
You’ll be able to
Explain legs of the traffic pattern
Recognize radio calls at nontowered airports
Traffic Pattern
Notes: Airport traffic patterns are developed to ensure that air traffic is flown into and out of an airport safely. Each airport traffic pattern is established based on the local conditions, including the direction and placement of the pattern, the altitude at which it is to be flown, and the procedures for entering and exiting the pattern.
It is imperative that pilots are taught correct traffic pattern procedures and exercise constant vigilance in the vicinity of airports when entering and exiting the traffic pattern

## Slide 3
Traffic Pattern
A standard path used to maintain order
Traffic Pattern
  Standard pattern is all LEFT turns
Notes: At an airport, the pattern is a standard path for coordinating airplane traffic. It differs from "straight-in approaches" and "direct climb-outs" in that aircraft using a traffic pattern remain close to the airport.
Patterns are usually employed at small general aviation (GA) airfields and military airbases. Many large controlled airports avoid the system unless there is GA activity as well as commercial flights.
Describe the typical traffic pattern including:
Upwind leg. A flight path parallel to and in the direction of the landing runway. It is offset from the runway and opposite the downwind leg.
Crosswind leg. A short climbing flight path at right angles to the departure end of the runway.
Downwind leg. A long level flight path parallel to but in the opposite direction of the landing runway. Maintain at least ½ mile offset from the runway. Certainly a plane giving a position report of "mid-downwind" can be visually located easily. When you're abeam the touchdown point on your downwind leg, it's time to start your descent to land. You start your descent by reducing the throttle, adding flaps, and pitching down to maintain your airspeed. Again, all airplanes are different, but in a Cessna 172, this usually means reducing the throttle to roughly 1500-1600 RPMs, adding 10 degrees of flaps, and pitching for 90 knots.
Base leg. A short descending flight path at right angles to the approach end extended centerline of the landing runway. When you're approximately 45-degrees from the touchdown point, it's time to make your base leg turn. You do it by entering a medium-banked turn until you're flying a perpendicular track to the runway. Remember, you want your ground track to be perpendicular to the runway, so if there's wind, you'll need to add some crab angle to make sure you aren't drifting away from the runway.
Final approach. A descending flight path in the direction of landing along the extended runway centerline from the base leg to the runway. The last section of the final approach is sometimes referred to as short final. As you start to approach the extended centerline of the runway, you'll start your medium banked base-to-final turn toward the runway. If you time it right (this is one of the more challenging things in flying) you'll roll out of your turn perfectly on the centerline.
Departure leg, Initial, or Climb out. The climbing flight path along the extended runway centerline which begins at takeoff and continues to at least 1/2 mile beyond the runway's departure end and not less than 300 feet below the traffic pattern altitude.
The names of the legs are logical and based on the relative wind as seen looking down a runway facing into the wind. An aircraft flying upwind heads into the wind, flying crosswind heads across the wind, flying downwind heads in the direction of the wind just like blown smoke.

## Slide 4
Like a Road in the Sky
Traffic Pattern
Notes: Describe the entry and departure in a traffic pattern.
Explain the fact that “left hand” patterns are the norm.
Unless otherwise specified, the standard recommended pattern height is 1000 ft AGL (above ground level), although a pattern height of 800 ft AGL is common. Helicopters usually fly the pattern at 500 ft AGL. Extreme caution must be exercised by pilots while flying at or through published traffic pattern altitudes as this might contribute to mid-air collisions.
So why do you fly a 45-degree angle to enter the downwind leg? By flying at an angle, it gives you (and others) good visibility to any other airplanes in the traffic pattern. And if you do see another airplane near you, it's easy to turn away from the airport, circle around, and make your 45-degree entry again.

## Slide 5
Why a Standard Pattern?
  Enter and depart airports on a predictable path
  Simplifies radio communication, even at nontowered airfield
    Whom you’re talking to
    Who you are
    Where you are
    Your intentions
    Repeat whom you're talking to
Traffic Pattern
Notes: Traffic patterns can be defined as left-hand or right-hand according to which way the turns in the pattern are performed. They are usually left-hand turns because most small airplanes are piloted from the left seat (or the senior pilot or pilot in command sits in the left seat), and so the pilot has better visibility out the left window. Right-hand patterns will be set up for parallel runways, for noise abatement, or because of ground features (such as terrain, towers, etc.).
If it is not otherwise stated, the patter is automatically a left-hand pattern. You can see if a runway uses a right-hand pattern on a sectional chart or chart supplement.

## Slide 6
Activity
Traffic Pattern Practice
    Use your aircraft type and tail number to identify who’s talking
    Examples:
      “Cessna N695JL, taking off on runway 22”
      “Cessna 5JL, turning left crosswind, runway 22”
Traffic Pattern
Notes: A fun addition to this activity is to create a “runway” and draw the traffic pattern legs on the ground. Have participants walk around the traffic pattern and use the script to make proper radio calls as they move around the pattern.
To practice take off and landings, a pilot would often fly many patterns, one after another, from the same runway. Upon each landing, depending on the runway distance remaining, aircraft and pilot capabilities, noise abatement procedures in effect, and air traffic control clearance, the pilot will perform either a full stop landing (taxi to the runway beginning for subsequent take-off), a touch-and-go (stabilize in the landing roll, reconfigure the aircraft for take-off, and take-off without ever stopping the aircraft), or a stop-and-go (decelerate to a stop, then take-off from the remaining runway). In the U.S., when operating in a controlled airport a pilot can be cleared for the option, allowing any of the landing options above, or a rejected landing, at pilot's discretion.
Explain and give some examples of what a pilot will say at each point in the traffic pattern shown.
In some cases, may want to overfly the airport before you enter the traffic pattern. Why would want to do that? It's a good way to check the airport and runway conditions, and to see if other airplanes are operating at the airport (they may not be using the CTAF frequency). Finally, if the airport doesn't have an automated weather reporting station (like ASOS), overflying is a good way to check out the windsock and make sure you're choosing the best runway to land on. If you do overfly the airport, you'll want to do it at 500-1000 feet above the traffic pattern. And while you're overflying, you also want to make radio calls on CTAF, announcing your current position, as well as what you're planning to do.

## Slide 7
Objectives
Traffic Pattern
You can now
Explain legs of the traffic pattern
Recognize radio calls at nontowered airports

## Slide 8
Questions?
The development of this program was made possible in part by a generous donation from the Sporty’s Foundation.
Traffic Pattern